## Slide 1
Design of steel frames with buckling restrained braces
M. Bosco, E.M. Marino, P. P. Rossi
Department of Civil and Environmental Engineering
University of Catania

## Slide 2
Buckling Restrained Braces (BRBs)
Design of steel frames with buckling restrained braces <number>/16
The Eurocode 8 does not stipulate provisions for the design of frames equipped with BRBs
yielding core
restrained
non-yielding segment
unrestrained
non-yielding segment
0.5 Lj
0.5 Lt
Lc
Lw
0.5 Lt
0.5 Lj
- No buckling, same behavior in tension and compression
- High ductility and dissipation capacity
- Extensively studied in the last decades
Advantages of BRBs
Notes: <number>

## Slide 3
Aim of the study
Design of steel frames with buckling restrained braces <number>/16
To define a Force-based method for the design of frames with BRBs within the framework of EC8
q
d
Input data:
To calibrate a proper value of the behavior factor q
q = behavior factor (should be stipulated by the code)
d = design story drift (assumed by the designer)
it reduces seismic force taking into the ductility of the structure
- it quantifies the ductility capacity of BRB max
- max  2 d/ y according to AISC 2005
Notes: <number>

## Slide 4
Design of BRBs
Design of steel frames with buckling restrained braces <number>/16
Design seismic forces Fi evaluated by the response spectrum reduced by q provide the yielding of the core of the BRBs
Fi

Yielding
Fi
Ny,i
Ny,i
Area of the core cross-section
Notes: <number>

## Slide 5
Design of non-dissipative elements (columns)
Design of steel frames with buckling restrained braces <number>/16
It is assumed that all BRBs are fully yielded and hardened
Pn
Pi-1
Pi
 Ny,n
 Ny,i+1
NEd,i

max
Ny
Nu
N
BRB modeling
Based on results of Merrit, 2006 Newell 2006:
 = 1.75 for max=15
Notes: <number>

## Slide 6
Design of non-dissipative elements (columns)
Design of steel frames with buckling restrained braces <number>/16
It is assumed that all BRBs are fully yielded and hardened
Pn
Pi-1
Pi
 Ny,n
 Ny,i+1
NEd,i
Notes: <number>

## Slide 7
Calibration of the q-factor
Design of steel frames with buckling restrained braces <number>/16
- A set of frames with BRBs is designed by several values of q-factor
24.0 m
24.0 m
8.0 m
8.0 m
3.3 m
8.0 m
Heigth: 4, 8 and 12 stories
BRBs:
Steel grade S235
Design drift d = 1.5%
PGA = 0.35 g
SoilC
q = 2.5 – 6.5 in step of 1.0
Seismic excitation (EC8):
Seismic excitation
Notes: <number>

## Slide 8
Calibration of the q-factor
Design of steel frames with buckling restrained braces <number>/16
- A set of frames with BRBs is designed by several values of q-factor
- The seismic response of these frames is evaluated by nonlinear dynamic analysis
The largest value of q that leads to acceptable seismic performance* of the analyzed frames is assumed as adequate
* Life safety performance level for 10%/50 year probability of exceedance
Notes: <number>

## Slide 9
Evaluation of the seismic performance
Design of steel frames with buckling restrained braces <number>/16
- Each frame was subjected to the 20 ground motions used in FEMA/SAC project corresponding to probability of exceedance of 10% in 50 years scaled by 90%
Maximum demand to capacity ductility ratio
Maximum ratio of column bending moment to moment resistance reduced due to the axial force
Maximum ratio of column axial force to buckling resistance reduced due to the bending moment
- The median over the 20 accelerograms is assumed as index of performance
- For each accelerogram is evaluated (at each story):
Notes: <number>

## Slide 10
Ductility demand of braces
Design of steel frames with buckling restrained braces <number>/16
 = maximum value of ductility demand of brace
max = ductility capacity of BRB
(ductility that BRB have to possess to accommodate a story drift equal to 2 d)
Ductility ratio
LS = ductility of BRB corresponding to the Life Safety limit state
(assumed as 3/4 max in analogy to the EC8 provision for beams)
BRB achieves the Life Safety limit state
Notes: <number>

## Slide 11
Ductility demand of braces
Design of steel frames with buckling restrained braces <number>/16
0
2
4
6
8
10
12
0.0
0.5
1.0
1.5
N

N
0
2
4
6
8
0.0
0.5
1.0
1.5

N
0
2
4
0.0
0.5
1.0
1.5

0
1
2
3
4
5
6
7
q
4-story frames

max
0
1
2
3
4
5
6
7
q
8-story frames

max
0
1
2
3
4
5
6
7
q
12-story frames

max
 5.5
 5.1
 6.1
max
max
max
Designed by:
q = 2.5
q = 3.5
q = 4.5
q = 5.5
q = 6.5
Notes: <number>

## Slide 12
24.0 m
24.0 m
8.0 m
8.0 m
Strength demand of columns
Design of steel frames with buckling restrained braces <number>/16
Columns of braced frames
(CBF columns)
Gravity columns
During the erthquake, columns sustain also bending moment because they are continuos over two stories
Seismic excitation
Notes: <number>

## Slide 13
Evaluation of the seismic performance
Design of steel frames with buckling restrained braces <number>/16
M = bending moment of column
MN,Rd = moment resistance reduced due to the axial force N (according to the EC3)
Normalized bending moment demand =
N = axial force of column
NM,Rd = buckling resistance reduced due to bending moment M (according to the EC3)
Normalized axial force demand =
Notes: <number>

## Slide 14
Columns of braced frame
Design of steel frames with buckling restrained braces <number>/16
0
2
4
6
8
10
12
0.0
0.5
1.0
N
M / M
N,Rd
0
2
4
6
8
0.0
0.5
1.0
N
M / M
N,Rd
1.5
0
2
4
0.0
0.5
1.0
N
M / M
N,Rd
0
2
4
6
8
10
12
0.0
0.5
1.0
N
N / N
M,Rd
0
2
4
6
8
0.0
0.5
1.0
N
N / N
M,Rd
1.5
0
2
4
0.0
0.5
1.0
N
N / N
M,Rd
Designed by:
q = 2.5
q = 3.5
q = 4.5
q = 5.5
q = 6.5
This conditions do not influence the behavior factor
Notes: <number>

## Slide 15
Gravity columns
Design of steel frames with buckling restrained braces <number>/16
0
2
4
6
8
10
12
0.0
0.5
1.0
N
M / M
N,Rd
0
2
4
6
8
0.0
0.5
1.0
N
M / M
N,Rd
1.5
0
2
4
0.0
0.5
1.0
N
M / M
N,Rd
0
2
4
6
8
10
12
0.0
0.5
1.0
N
N / N
M,Rd
0
2
4
6
8
0.0
0.5
1.0
N
N / N
M,Rd
1.5
0
2
4
0.0
0.5
1.0
N
N / N
M,Rd
Designed by:
q = 2.5
q = 3.5
q = 4.5
q = 5.5
q = 6.5
This conditions do not influence the behavior factor
Notes: <number>

## Slide 16
Conclusions
The proposed method for design of frames with BRBs seems to be suitable if applied with a value of q = 5
The analysis has been repeated by other value of d and the following relation has been obtained*
* M. Bosco and E.M. Marino Design Method and Behavior Factor for Steel Frames with Buckling Restrained Braces, submitted to Earthquake Engineering and structural Dynamics
Design of steel frames with buckling restrained braces <number>/16
q = 400 Δd (%) – 1.0
The behavior factor q = 5 is valid if a design story drift d = 1.5% is assumed

## Slide 17
Thank you for your attention