## Slide 1: THE 14th WORLD CONFERENCE ON EARTHQUAKE ENGINEERING October 12-17, 2008, Beijing, China
A design method for the seismic upgrade of existing r.c. frames by buckling restrained braces
Melina Bosco, Aurelio Ghersi, Edoardo M. Marino
Department of Civil and Environmental Engineering, University of Catania

## Slide 2: Typical deficiencies of existing r.c. framed structures
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
The distribution of the shear strength along the height of existing r.c. frames often promotes a soft storey mechanism
The distributions of the lateral stiffness and shear strength along the height are not suitable to make the displacement/deformation demand consistent with the capacity of the frame.
Because main structural elements are usually disposed along a single direction, these structures are very flexible and weak in the orthogonal direction.

## Slide 3: Improving seismic behaviour of existing r.c. framed structures by BRBs
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Mortar
Steel core
Unbounding agent
Steel casing
Cyclic behaviour
F


## Slide 4: Improving seismic behaviour of existing r.c. framed structures by BRBs
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
modify the distribution of the shear strength along the height so as to promote a widespread yielding during strong ground motions;
modify the distribution of the lateral stiffness along the height so that the displacements demanded by the ground motion can better fit the displacement capacity of the structure.
increase both the total lateral stiffness and the shear strength of the structure to proper values;
The insertion of BRBs can:

## Slide 5: Aim of the paper
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Propose a design method for the seismic rehabilitation of existing r.c. frames by BRBs;
Perform a preliminary calibration of the parameters which control the proposed design method.

## Slide 6: Proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Displacement requirement
aims at reducing the displacement demand below the value corresponding to the considered limit state;
determines the lateral stiffness provided by BRBs.
Strength requirement
stipulates a minimum lateral strength distributed along the height proportionally to the story shear demanded by the design ground motion;
determines the lateral strength provided by BRBs.
It is based on two requirements

## Slide 7: Lateral stiffness provided by BRBs
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
l,i
hi
l,i
l,i = (l,i + y,i) hi
l,i
Plastic rotation corresponding to the selected limit state
y,i
Chord rotation at yielding
The storey drift i demand is determined by an elastic analysis based on the elastic (unreduced) spectrum of the reference ground motion.
The storey drift l,i capacity is determined by the limit analysis assuming a story collapse mechanism.

## Slide 8: Lateral stiffness provided by BRBs
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
The storey drift i demand is determined by an elastic analysis based on the elastic (unreduced) spectrum of the reference ground motion.
The storey drift l,i capacity is determined by the limit analysis assuming a story collapse mechanism.
The lateral stiffness of BRBs Kb,i is equal to the total required stiffness KTot,i minus that of the r.c. frame Kf,i.
ratio of the total story shear force (determined by elastic analysis) to the design storey drift d,i (obtained reducing l,i).
ratio of the story shear force sustained by the columns to the storey drift demand i.
KTot,i
Kf,i

## Slide 9: Lateral strength provided by BRBs
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
The total required lateral strength is equal to the story shear VSd,i evaluated by the elastic analysis based on the design spectrum (elastic spectrum reduced by q).
The available lateral strength of the r.c. frame Vf Rd,i is obtained as the story shear transmitted by the columns in the story mechanism.
Fi
MRd,ij
MRd,ij
VRd,ij
VRd,ij
Vf Rd,i=VRd,ij

## Slide 10: Lateral strength provided by BRBs
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
The total required lateral strength is equal to the story shear VSd,i evaluated by the elastic analysis based on the design spectrum (elastic spectrum reduced by q).
The lateral strength that has to be provided by the BRBs Vb Rd,i is equal to VSd,i minus Vf Rd,i.
The available lateral strength of the r.c. frame Vf Rd,i is obtained as the story shear transmitted by the columns in the story mechanism.

## Slide 11: Application of the proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
A r.c. frame designed to resist only gravity loads is upgraded by BRBs designed by the proposed method.
r.c. frame
Story
Col. 1 and 4
Col. 2 and 3
Beams
6th
30x30
30x30
30x60
5th
30x30
30x30
30x60
4th
30x30
30x30
30x60
3rd
35x30
30x40
30x60
2nd
40x30
30x50
30x60
1st
50x30
30x60
30x60
Cross-section dimensions (cm)
4 m
4 m
4 m
3.2 m
BRBs

## Slide 12: Application of the proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
A r.c. frame designed to resist only gravity loads is upgraded by BRBs designed by the proposed method.
The elastic spectrum proposed by the EC8 for soil type C and PGA=0.35 g is used as seismic input.
Several values of the design parameters are considered:
di = 1.00, 0.75, 0.50 and 0.25 l,i
q = 6.7, 5.0, 4.0 and 3.3
The life safety limit state is used as target limit state.

## Slide 13: Required stiffness and strength of BRBs Cases: d,i < 0.50 l,i
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Lateral strength (kN)
Lateral stiffness (kN/mm)
BRBs, q=3.3
RC frame
BRBs, q=4.0
BRBs, q=5.0
BRBs, q=6.7
0
200
400
1
5
3
2
6
4
N
Ki
For d,i< 0.50 l,i, the design of the BRBs is always controlled only by the strength requirement.
The required lateral strength increases as q decreases; for q=3.3 the required strength of BRBs is much larger than that of the r.c. frame.
0
500
1000
1
5
3
2
6
4
N
VRdi

## Slide 14: Required stiffness and strength of BRBs Cases: d,i < 0.50 l,i
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Lateral strength (kN)
0
500
1000
1
5
3
2
6
4
N
VRdi
Lateral stiffness (kN/mm)
BRBs, q=3.3
RC frame
BRBs, q=4.0
BRBs, q=5.0
BRBs, q=6.7
0
200
400
1
5
3
2
6
4
N
Ki
The adopted value of q influences also the required stiffness of BRBs, which increases as q decreases.

## Slide 15: Required stiffness and strength of BRBs Case: d,i = 0.50 l,i
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Lateral strength (kN)
Lateral stiffness (kN/mm)
BRBs, q=3.3
RC frame
BRBs, q=4.0
BRBs, q=5.0
BRBs, q=6.7
0
200
400
1
5
3
2
6
4
N
Ki
For d,i = 0.50 l,i both the required stiffness and strength of BRBs are larger than those obtained for smaller values of d,i, especially for small values of q.
0
500
1000
1
5
3
2
6
4
N
VRdi

## Slide 16: Required stiffness and strength of BRBs Case: d,i = 0.25 l,i
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Lateral strength (kN)
Lateral stiffness (kN/mm)
BRBs, q=3.3
RC frame
BRBs, q=4.0
BRBs, q=5.0
BRBs, q=6.7
0
200
400
1
5
3
2
6
4
N
Ki
For d,i = 0.25 l,i the required stiffness and strength of BRBs drastically increase.
0
500
1000
1
5
3
2
6
4
N
VRdi

## Slide 17: Validation of the proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Each frame is subjected to 10 artificial accelerograms compatible with the elastic response spectrum used in design (EC8 spectrum soil type C, ag=0.35g).
The seismic response is determined by nonlinear dynamic analysis by DRAIN-2DX computer program.
For each accelerogram is evaluated:
inter-story drift demand i;
inter-story drift capacity l,i;
inter-story drift demand to capacity ratio i /l,i.
The mean value of each parameter is evaluated.

## Slide 18: Validation of the proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
0
2
4
6
0
25
50
75
100
125
N
q = 6.7
q = 4.0
q = 5.0
q = 3.3
i (mm)
0
2
4
6
0
25
50
75
100
125
N
q = 6.7
q = 4.0
q = 5.0
q = 3.3
i (mm)
Drift demand (d,i > 0.50 l,i)
Drift capacity (d,i > 0.50 l,i)
The storey drift demand becomes uniform along the height and decreases when smaller values q are used.
But, also the storey drift capacity decreases when smaller values q are used.

## Slide 19: Validation of the proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
d,i > 0.50 l,i
d,i = 0.50 l,i
For d,i > 0.5 l,i, the drift demand to capacity ratio is acceptable for q not larger that 4.
For d,i = 0.5 l,i, the performance of the frame is acceptable regardless of the adopted value of q.
0
2
4
6
0
0.5
1.0
1.5
N
i/l,i
q = 6.7
q = 4.0
q = 5.0
q = 3.3
N
0
2
4
6
0
0.5
1.0
1.5
i/l,i
q = 6.7
q = 4.0
q = 5.0
q = 3.3

## Slide 20: Validation of the proposed design method
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
0
2
4
6
0
0.5
1.0
1.5
N
q = 6.7
q = 4.0
q = 5.0
q = 3.3
i/l,i
d,i = 0.50 l,i
d,i = 0.25 l,i
The use of d,i = 0.25 l,i provides a further (but slight) improvement of the seismic behaviour of the frame.
0
2
4
6
0
0.5
1.0
1.5
N
q = 6.7
q = 4.0
q = 5.0
q = 3.3
i/l,i

## Slide 21: Conclusions
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
When d,i is taken larger than 0.5 l,i the r.c. frame upgraded by BRBs meets the Life Safety limit state verification only if a value of q not larger than 4 is used.
If d,i is taken not larger than 0.5 l,i even the largest considered value of q (6.7) can be adopted.
A design method for upgrading existing r.c. frames, designed to sustain only gravity loads, by BRBs is defined and a strategy for its calibration is proposed.

## Slide 22
Seismic upgrade of existing r.c. frames by BRBs
<number>/22
Thanks for your attention